Prindle Pond Water Testing (August, 2021)

Date: August 3, 2021

Weather:  Sky – P.Cloudy 60's

Daytime Avg.Temp (48hrs). –  70's, Weather (48hrs) –  P. Cloudy/Some Rain

| Site | Depth (M)) | Temp (C) | Temp (F) | RDO (mg/L) | pH | Cond. (uS/cm) | Turb. (NTU) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Tom Cove | 0.5 | 23.39 | 73 | 8.43 | 8.04 | 130.5 | 2.9 |
| John/Jeff | 0.5 | 23.12 | 73 | 8.09 | 8.03 | 131.2 | 2.6 |
| Dam | 0.5 | 23.19 | 73 | 9.16 | 8.05 | 130 | 3.4 |
| Dam | 1.5 | 23.21 | 73 | 8.55 | 8 | 129.2 | 1.9 |
| Hope | 0.5 | 23.46 | 74 | 8.41 | 7.99 | 130.8 | 2.4 |
| Kevin J. | 0.5 | 23.09 | 73 | 9.23 | 8 | 130.3 | 2.7 |
| Jan | 0.5 | 23.14 | 73 | 8.61 | 8.07 | 131.2 | 2.2 |
| Watts | 0.5 | 23.64 | 74 | 8.85 | 7.97 | 130.6 | 2.6 |
| Jason | 0.5 | 23.1 | 73 | 8.41 | 8.08 | 130.8 | 2.7 |
| Secchi | 1.8 |  |  |  |  |  |  |

|  | Secchi (M) | Temp.C | RDO mg/L | pH | uS/cm | NTU |
| --- | --- | --- | --- | --- | --- | --- |
| Excellent Readings | > 4.5 | <25.0 | >/= 6 | 6.5 – 8.0 | <120 | 0-1.0 |
| Good Readings | 3 to 4.5 | </= 27 | 5 to 6 | 6.5 - 8.5 | >120.1 | 1.1.—5.0 |
| Fair Readings | 1.2 to 3 | </= 28.3 | 4 to 5 | 6.0 - 9.0 | >240 | 5.1.-- 10 |
| Poor Readings | < 1.2 | >28.3 | <4 | <6.0, >9.0 | >360 | >10 |

Secchi and Turbidity (NTU)  – Measure of the cloudiness in the water, can be caused by soil erosion, run-off, waste discharge, algal growth, boat traffic and pollen.

Temperature (C) – Measure of the temperature of water which has an impact on the dissolved oxygen, weed and algal growth, and the fish.

Dissolved oxygen (mg/L) – Measure of dissolved oxygen, colder water holds more oxygen, fish become stressed at levels below 4mg/L.  At 10C – 11.3 mg/L, at 30C – 7.5mg/L

pH - Measure of the acid/alkaline relationship in a water body.

Conductivity (uS/cm) – Measure of dissolved inorganic solids such as road salt, fertilizers, or contaminants from a failed septic system.